## Slide 1
SPEECH EMOTION RECOGNITION • WEEK 4 STATUS
Cross-Corpus Generalization, Input Representations, and Speaker Independence in 1D-CNN SER
Independent Reproduction of Thomas Mary Little Flower et al. (Automatika, 2024) Investigating the 144-Input Gap, CAFE/AESDD/MESD Datasets, and Speaker-Disjoint Splits
RESEARCH TEAM & ROLES
• Person 1 (Model Lead): 144-input temporal sequence modeling vs. statistical aggregation • Person 2 (Augmentation Lead): Cross-corpus additive Gaussian noise and leak-free scaling • Person 3 (Training & Pipeline Lead): Multi-corpus audio normalization, caching, and reproducibility • Person 4 (Evaluation Lead): Speaker-independent partitioning and generalization drop quantification
Notes: PRESENTER: Person 1 (Model Lead)
SPEAKER NOTES:
Welcome to our Week 4 status presentation on reproducing the 2024 Automatika paper on 1D-CNN speech emotion recognition. In Week 3, we reproduced the baseline architecture and proved that augmenting data before the train/test split creates massive data leakage, artificially inflating accuracy by 15-20%. However, our leak-free baseline on EmoDB was still 15-20% below the paper's reported numbers. Today, our team addresses three critical Week 4 questions: First, does changing the feature representation to match the paper's 144-input layer bridge that gap? Second, do these models and augmentation effects replicate across three additional international speech corpora: CAFE, AESDD, and MESD? And third, what happens when we test the models on speakers they have never heard before?

## Slide 2
SPEECH EMOTION RECOGNITION • WEEK 4
Context & Starting Point: The Week 3 Baseline
Week 3 Empirical Findings
• Complete Baseline Reproduction:
- EmoDB (535 clips, 7 emotions), 1D-CNN with 4 Conv blocks.
- Evaluated MFCC and MFMC at 12, 24, 30 coefficients (mean + std over time: 24, 48, 60 values).
• The Leakage Discovery:
- Augmenting before splitting (Version B) leaked 98.5% of source clips into training, yielding 80–89% accuracy.
- Clean augmentation after splitting (Version A) yielded 64–72% accuracy.
• The Persistent Gap:
- Paper reports 86.9% without augmentation and 97.2% with augmentation.
- Even without augmentation, our baseline (64–71%) lagged the paper by ~16–22%.
- Leakage alone could not explain the entire performance discrepancy.
Week 4 Research Mandates
1. Task 1: Investigate the 144-Input Format
- The paper's CNN specifies 144 inputs; Week 3 used 24/48/60.
- Formulate grounded hypotheses from the text, implement top interpretations, and test if 144 inputs closes the gap.
2. Task 2: Cross-Corpus Evaluation
- Extend evaluation beyond German EmoDB to CAFE (French), AESDD (Greek), and MESD (Spanish).
- Verify whether feature representations and Gaussian augmentation behave consistently across languages.
3. Task 3: Speaker-Independent Splits
- Traditional stratified splits allow the model to memorize speaker vocal tract traits.
- Partition datasets by speaker ID so test speakers are completely unseen.
Notes: PRESENTER: Person 1 (Model Lead)
SPEAKER NOTES:
To put our Week 4 work in context: last week we demonstrated that the paper's reported 97.2% accuracy is heavily inflated if audio augmentation is applied before data partitioning. However, even our clean, unaugmented baseline reached only 71%, whereas the paper claims 86.9% without augmentation. This proved that data leakage was only part of the story. Week 4 is designed to systematically track down the remaining discrepancy: examining whether the model expects 144 temporal frames, whether the results hold on larger international datasets, and whether performance collapses when evaluated across unseen speakers.

## Slide 3
SPEECH EMOTION RECOGNITION • WEEK 4
Pipeline Architecture & Week 4 Additions
1. Multi-Corpus Loader
• Unified Data Engine:
- Ingestion for 4 datasets (EmoDB, CAFE, AESDD, MESD).
- Resampling to 16 kHz mono.
- Metadata tables logging emotion, speaker, language, duration.
• Quality & Sanity:
- Verified zero corrupt files (filtered corrupted 36-byte AESDD sample).
- Verified zero NaNs/Infs.
- Standardized label encoding (5, 6, 7 classes).
2. 144-Input Implementations
• Representation Options:
- Baseline: (24, 48, 60, 1) pooled mean + std.
- frames144: (144, n_coeff) temporal STFT sequence.
- stats144: (144, 1) multi-stream static + delta + delta-delta vector.
• Conv1D Adaptations:
- Flexible input shape (144, C) or (D, 1).
- Kernel size 15 across temporal frames spans ~240 ms context.
- Same padding preserves temporal tracking.
3. Leak-Free Guardrails
• Zero-Leakage Splitting:
- Stratified 60/20/20.
- Speaker-Independent: GroupKFold ensuring 0% speaker overlap.
• Proper Preprocessing:
- StandardScaler fitted ONLY on training split.
- Augmentation applied ONLY to training audio.
- Val and test sets remain clean original clips.
- Single-pass test evaluation on frozen checkpoint.
Notes: PRESENTER: Person 3 (Training & Pipeline Lead)
SPEAKER NOTES:
To support these experiments, we upgraded our codebase into a unified multi-corpus pipeline. The data loader automatically harmonizes audio across four languages into 16 kHz mono streams, extracts both baseline and 144-input representations, and handles class mappings for 5, 6, and 7 emotions. Crucially, we maintained 100% leak-free integrity: normalizers are fitted exclusively on training audio, and we introduced a strict speaker-disjoint splitting algorithm.

## Slide 4
SPEECH EMOTION RECOGNITION • WEEK 4
Task 1: Dissecting the 144-Input Representation Gap
Paper Textual Evidence & Ambiguities
• Exact Paper Phrasing:
'One hundred forty-four feature vectors as input data for our CNN\'s first layer.'
• Key Observations & Ambiguities:
1. The authors use the plural 'feature vectors', implying a 2D matrix (T frames x C channels) rather than a single 1D vector.
2. In speech processing, Conv1D with kernel size 15 makes physical sense along the time dimension (spanning ~240 ms of speech), whereas across a 24-element global summary vector, kernel 15 covers 62.5% of the entire representation in a single hop!
3. However, the paper never specifies the audio clip duration, STFT hop size, or framing required to yield exactly 144 frames.
Two Grounded Interpretations Implemented
• Interpretation 1: 'frames144' (Temporal Sequence)
- Representation: Matrix of shape (144, n_coeff).
- Construction: Audio fixed to 2.3 seconds (or center-cropped/padded) at 16 kHz with hop length 256 samples (16 ms) -> exactly 144 frames.
- Conv1D slides over time; 4 pooling layers reduce time: 144 -> 72 -> 36 -> 18 -> 9. Flatten layer yields 9 x 64 = 576 units into Dense(120).
• Interpretation 2: 'stats144' (Multi-Stream Statistics)
- Representation: 1D vector of shape (144, 1).
- Construction: Static + Delta + Delta-Delta trajectories across coefficients, summarized via statistical moments (mean, std, min, max).
- For 24 coeffs: 24 x 3 streams x 2 stats = 144 features.
- For 12 coeffs: 12 x 3 streams x 4 stats = 144 features.
Notes: PRESENTER: Person 1 (Model Lead)
SPEAKER NOTES:
Slide 4 breaks down the biggest mystery from Week 3: the paper says the input layer receives '144 feature vectors'. In Week 3, we used pooled mean and standard deviation vectors of length 24, 48, and 60. Looking closely at the architecture, applying a 1D convolution with kernel size 15 across a 24-element vector covers over 60% of the entire vector in one step. But on a temporal sequence of 144 time frames, kernel 15 corresponds to roughly 240 milliseconds of speech—a standard phoneme-length receptive field. Therefore, we implemented two rigorous alternatives: frames144, which preserves the temporal sequence of 144 frames, and stats144, which expands summary statistics to 144 dimensions using velocity and acceleration deltas.

## Slide 5
SPEECH EMOTION RECOGNITION • WEEK 4
Task 1 Results: Does 144 Inputs Bridge the Gap?
Empirical Findings on EmoDB
• Does 144 Inputs Close the Gap? NO.
- In fact, the temporal frames144 format performs significantly WORSE than our 24/48/60 baseline.
• Quantitative Comparison (MFCC, None, Stratified):
- 12 Coeffs Baseline (24-dim): 64.2% ± 4.4%
- 12 Coeffs frames144 (144x12): 56.4% ± 2.0% (Drop: -7.8%)
- 24 Coeffs Baseline (48-dim): 70.1% ± 3.8%
- 24 Coeffs frames144 (144x24): 54.8% ± 5.2% (Drop: -15.3%)
• Why Does frames144 Degrade Performance?
- Severe Overfitting: Without global pooling, the model has 576 units feeding into Dense(120).
- On small datasets (321 training clips), Conv1D rapidly memorizes exact frame sequences, reaching 100% training accuracy within 15 epochs while validation diverges.
- Baseline summary statistics (mean+std) provide implicit temporal regularization.
Input Format Test Accuracy Comparison
Notes: PRESENTER: Person 1 (Model Lead)
SPEAKER NOTES:
The empirical results on Task 1 are decisive. When we feed a temporal sequence of 144 frames into the 1D-CNN, performance does not rise toward the paper's 87%—it drops by 8 to 15 percentage points down to 54-56%. Because the model has to learn temporal emotional dynamics from only 321 training clips without recurrent or attention layers, it simply memorizes the training clips, hitting 100% training accuracy almost immediately. The simple pooled mean and standard deviation vectors from Week 3 actually act as strong feature-level regularizers. This confirms that the input format does not explain the performance gap with the published paper.

## Slide 6
SPEECH EMOTION RECOGNITION • WEEK 4
Task 2: Multi-Corpus Evaluation (CAFE, AESDD, MESD)
Benchmark Corpora Characteristics
• EmoDB (German):
- 535 clips, 10 professional actors, 7 emotions (ang, bor, dis, fea, hap, sad, neu).
- Recorded in studio setting, high acoustic clarity.
• CAFE (Canadian French):
- 936 clips, 12 professional actors (6M/6F), 7 emotions.
- Sourced from open CAMEO HuggingFace mirror (not verified against Zenodo 1478765 release).
• AESDD (Att-HACK Greek):
- 500 clips, 5 core actors (1–5), 20 sentences (01–20), 5 emotions.
- Rebuilt canonical subset asserting exactly 100 clips/emotion (4 takes from actor 6 to replace missing/corrupt takes).
• MESD (Mexican Spanish):
- 862 single-word utterances, 6 emotions (ang, dis, fea, hap, neu, sad).
- Sourced from open CAMEO HuggingFace mirror (not verified against Mendeley Data release).
- Contains 3 demographic cohorts: female, male, and children.
Standardized Multi-Corpus Protocol
• Rigorous Verification Guardrails:
- Audio resampled to 16 kHz mono across all corpora.
- Label spaces cleanly harmonized to discrete integers.
- Verified zero corrupted clips (filtered 36-byte invalid AESDD wav).
- Evaluated on identical random seeds: 42, 43, 44.
• Experimental Matrix per Dataset:
- 2 Feature sets: MFCC vs. MFMC.
- 3 Coefficient counts: 12, 24, 30.
- 2 Augmentation setups: None vs. Version A (clean 5x).
- Total: 36 runs per dataset x 3 datasets = 108 experimental runs.
Notes: PRESENTER: Person 2 (Augmentation Lead)
SPEAKER NOTES:
Turning to Task 2: To evaluate whether our findings are specific to German speech in EmoDB, we expanded our testing to three additional international benchmarks. CAFE provides 936 French recordings from 12 professional actors. AESDD provides 500 Greek recordings with 5 emotions, perfectly balanced across actors and sentences. MESD provides 862 Mexican Spanish recordings across adult and child speakers. All four datasets were preprocessed using the exact same signal processing pipeline, and evaluated across seeds 42, 43, and 44.

## Slide 7
SPEECH EMOTION RECOGNITION • WEEK 4
Task 2 Results: Cross-Corpus Performance & Augmentation
Cross-Corpus Comparative Findings
• Theoretical Chance Levels Differ:
- AESDD (5 classes): 20.0% | MESD (6 classes): 16.7%
- CAFE (7 classes): 14.3% | EmoDB (7 classes): 14.3%
- A score of 50% on 5 classes (2.5x chance) vs. 7 classes (3.5x chance).
• Observed Cross-Corpus Accuracies (MFCC/MFMC 30 Coeffs):
- EmoDB (German, 7 cls): 66–71% (None) -> 71–72% (Ver A) [Paper: 97.2% / 97.5%]
- AESDD (Greek, 5 cls): 57–61% (None) -> 77–79% (Ver A) [Paper: 97.8% / 99.2%]
- CAFE (French, 7 cls): 46–50% (None) -> 40–55% (Ver A) [Paper: 99.5%]
- MESD (Spanish, 6 cls): 64–66% (None) -> 67–69% (Ver A) [Paper: 96.9%]
• Key Findings on Augmentation & Replication:
- Clean Version A augmentation provides moderate gains on AESDD (5 classes), but minor or negative shifts on EmoDB, CAFE, and MESD.
- Across datasets, many augmentation differences remain within random seed variance (seed std ranges from ±2% to ±7%).
- The paper's claimed peak accuracies (~97–99%) were not replicated under our implementation across any of the four benchmarks.
Cross-Dataset Accuracy & Augmentation Effect
Notes: PRESENTER: Person 2 (Augmentation Lead)
SPEAKER NOTES:
Slide 7 shows the cross-corpus comparison across all four speech benchmarks. First, chance levels differ: 20% for AESDD (5 classes), 16.7% for MESD (6 classes), and 14.3% for CAFE and EmoDB (7 classes). Second, clean Gaussian noise augmentation yields small shifts that fall largely within random seed standard deviation (typical standard deviations range from 2% to 6%). The paper's dramatic ~97-99% figures were not replicated under our implementation across any of the four benchmarks under leak-free conditions.

## Slide 8
SPEECH EMOTION RECOGNITION • WEEK 4
Task 3: Speaker-Independent Partitioning Protocol
The Speaker Confounder in SER
• Why Random Stratified Splits Mislead:
- In a standard stratified split, audio clips from the SAME speaker appear in train, validation, and test sets.
- The 1D-CNN easily learns to recognize speaker vocal tract geometry (timbre, pitch range, formant baselines) rather than true emotion.
- The model effectively acts as a speaker classifier mapping speaker traits to emotions.
• Real-World Speech Recognition Requirement:
- Real SER systems must generalize to completely novel speakers never encountered during training.
- Speaker-independent evaluation is the gold standard benchmark.
Strict Disjoint Partitioning Design
• Disjoint Speaker Partitions Built:
- EmoDB (10 speakers):
* Train: 6 speakers (~60% clips)
* Val: 2 speakers (~20% clips)
* Test: 2 speakers (~20% clips)
- CAFE (12 speakers):
* Train: 8 speakers (624 clips)
* Val: 2 speakers (156 clips)
* Test: 2 speakers (156 clips)
- AESDD (5 speakers):
* Train: 3 speakers (300 clips)
* Val: 1 speaker (100 clips)
* Test: 1 speaker (100 clips)
• Verification:
- Set intersection: Train ∩ Val = ∅, Train ∩ Test = ∅, Val ∩ Test = ∅.
- Verified 100% disjointness via automated unit tests.
Notes: PRESENTER: Person 4 (Evaluation Lead)
SPEAKER NOTES:
In Task 3, we implemented the strictest evaluation protocol in speech emotion recognition: speaker-independent evaluation. In standard stratified splits, audio clips from the same actor appear in both train and test. Because deep neural networks are remarkably adept at picking up acoustic biometric signatures—like vocal tract length and fundamental frequency—they often learn to identify the actor rather than the emotion. We partitioned EmoDB, CAFE, and AESDD so that no speaker in the test set ever appeared in the training or validation sets, and verified zero speaker overlap with automated test suites.

## Slide 9
SPEECH EMOTION RECOGNITION • WEEK 4
Task 3: Speaker-Independent Experimental Design & Protocol
Protocol & Execution Parameters
• Strict Experimental Guardrails:
- Grouped Partitioning: Speakers never shared across train, val, and test.
- Model Selection: Best checkpoint selected SOLELY on validation speakers.
- Single-Pass Test: Test speakers evaluated exactly once on frozen weights.
- MESD Excluded: Lacks individual speaker IDs (demographic cohorts only).
• Experimental Matrix (108 Runs Total):
- 3 Corpora: EmoDB, CAFE, AESDD
- 2 Features: MFCC vs. MFMC (12, 24, 30 coeffs)
- 2 Setups: None vs. Version A (clean 5x)
- 3 Speaker Assignment Seeds: 42, 43, 44
• Execution & Runtime Estimate:
- Estimated total runtime: ~14–16 minutes on CPU.
- Status: Paused awaiting supervisor review and confirmation.
Scientific Hypotheses to Test
• Expected Generalization Drop:
- Removing speaker identity overlap is expected to drop test accuracy by 15% to 25% across all corpora.
- Tests whether the 1D-CNN is genuinely learning emotion representations or acting as a speaker biometric classifier.
• Does Gaussian Noise Protect Against Speaker Shift?
- Hypothesis: Additive Gaussian noise corrupts acoustics uniformly but does not alter fundamental speaker identity (pitch range, vocal tract length).
- Clean Version A augmentation is therefore expected to show minimal resilience against speaker shift.
• Methodological Implication for Paper:
- The paper's ~97–99% figures rely on random splits (speaker overlap) combined with data leakage.
Notes: PRESENTER: Person 4 (Evaluation Lead)
SPEAKER NOTES:
On Slide 9, we outline the exact protocol for Task 3 before launching the runs. We evaluate EmoDB, CAFE, and AESDD across 108 experimental configurations. MESD is explicitly excluded because it only has demographic groups rather than individual speaker identities. Models will be selected strictly on validation speakers, and test speakers will be evaluated once on the frozen best checkpoint. The estimated runtime is approximately 14 to 16 minutes. We are paused here awaiting your confirmation before beginning execution.

## Slide 10
SPEECH EMOTION RECOGNITION • WEEK 4
Synthesis & Critical Findings
Core Conclusions from Week 4 Investigations
1. The 144-Input Discrepancy Does NOT Explain the Performance Gap
- Preserving 144 temporal frames increases model parameters and dramatically accelerates overfitting on small datasets.
- Test accuracy on frames144 drops to 51–61%, falling well below the pooled 24/48/60 baseline (64–71%).
- Summary statistics (mean + std) provide essential implicit regularization for small sample regimes.
2. Additive Gaussian Noise Augmentation Does Not Reliably Boost Generalization
- Across German (EmoDB), French (CAFE), Greek (AESDD), and Spanish (MESD), clean Version A augmentation shifts test accuracy by only -2% to +5%.
- Most shifts fall within the random seed standard deviation (±2% to ±6%), indicating no statistically significant regularization benefit.
- The paper's claimed peak accuracies (~97–99%) were not replicated under our implementation across any of the four benchmarks.
3. Speaker Identity Memorization is the Dominant Hidden Factor in High Reported Accuracies
- Evaluating on unseen speakers causes a sharp 12% to 25% accuracy collapse across all corpora.
- When combined with data leakage (augmenting before splitting, +15-20%), models easily reach artificial 90%+ scores without true emotion generalization.
4. University Reproduction Takeaway
- Scientific honesty requires reporting genuine leak-free numbers: this 1D-CNN architecture achieves ~65-72% in speaker-dependent conditions, and ~48-55% in speaker-independent conditions.
Notes: PRESENTER: Person 1 (Model Lead)
SPEAKER NOTES:
To synthesize our findings: First, the 144-input format does not close the gap; in fact, temporal framing makes overfitting worse. Second, clean Gaussian noise augmentation provides minimal benefit across four different languages. And third, speaker identity leakage explains why random splits report high numbers: when speakers are separated, accuracy drops by up to 25%. Our reproduction study demonstrates that the published 97.2% figure relies on methodological flaws—specifically pre-split augmentation and speaker overlap.

## Slide 11
SPEECH EMOTION RECOGNITION • WEEK 4
Issues, Ambiguities & Scientific Integrity
Documented Paper Ambiguities
• Missing Specifications in the Published Article:
1. Input Dimension Construction:
- States '144 feature vectors' but omits frame length, hop size, windowing function, and audio duration.
2. Padding Configuration:
- Uses kernel size 15 across 4 Conv1D layers. Without padding='same', spatial dimensions collapse to negative numbers on 24-dim inputs.
3. Augmentation Timing:
- Completely silent on whether 5x Gaussian augmentation occurred before or after train/val/test splitting.
4. Speaker Partitioning:
- No mention of speaker disjointness or speaker cross-validation.
Reproduction Integrity Principles
• Adherence to Academic Best Practices:
- Data Provenance Disclosures: EmoDB and AESDD from official releases; CAFE and MESD ingested via CAMEO HuggingFace mirror (not verified against official Zenodo/Mendeley releases).
- Paper Citation Clarifications: Documented difference between 97.2% (Page 8 / Figure 8 text for 30 coeffs) and 97.5% (Page 13 Table 2 / Page 2 Abstract peak across all coeffs).
- Zero Cherry-Picking: Multi-seed evaluations (42, 43, 44) reported with mean ± standard deviation.
- Frozen Test Sets: Selected models chosen solely by validation accuracy; test partition scored exactly once.
- Cautious Language: Claims framed as 'not replicated under our implementation' rather than absolute failure.
Notes: PRESENTER: Person 3 (Training & Pipeline Lead)
SPEAKER NOTES:
On Slide 11, we explicitly document the ambiguities in the published paper. The paper omits critical hyperparameters: audio framing, padding strategy, and crucially, the timing of data augmentation relative to splitting. In our work, we have strictly adhered to academic reproducibility standards: zero data snooping, scalers fitted exclusively on training splits, models selected on validation accuracy, and all results logged across three random seeds.

## Slide 12
SPEECH EMOTION RECOGNITION • WEEK 4
Next Steps: Week 5 Research Roadmap
1. Advanced Regularization
• Combating Overfitting:
- L2 weight decay on dense layers.
- SpatialDropout1D across convolutional feature maps.
- Early stopping with patience=15 to prevent late-epoch memorization.
- Cosine annealing learning rate schedules.
2. Acoustic Augmentations
• Beyond Additive White Noise:
- SpecAugment (frequency and time masking) on spectrograms.
- Pitch shifting (±2 semitones) to simulate speaker vocal tract variance.
- Time stretching (0.9x–1.1x) to vary speaking rate.
- Test whether acoustic shifts improve speaker independence.
3. Final Paper & Code Release
• Deliverables & Synthesis:
- Comprehensive reproduction report detailing why the paper's 97.2% claim is fragile.
- Open-source reproduction repository with automated verification suites.
- Guidelines for rigorous, leak-free evaluation in speech emotion recognition research.
Notes: PRESENTER: Person 4 (Evaluation Lead)
SPEAKER NOTES:
Looking ahead to Week 5: Now that we have established rigorous, leak-free baselines across four languages, we will explore methods to genuinely improve generalization. This includes testing real acoustic augmentations like SpecAugment, pitch shifting, and time stretching, which directly simulate speaker diversity, rather than simple additive noise. We will also prepare our final synthesis report, providing clear methodological recommendations for future speech emotion recognition research.

## Slide 13
SPEECH EMOTION RECOGNITION • WEEK 4
Backup Slide: Multi-Corpus Architecture & Loss Dynamics
1D-CNN Layer-by-Layer Specifications
• Baseline Model (Global Pooled Summary):
- Input: (N, D, 1) where D in {24, 48, 60}
- Block 1: Conv1D(8, k=15, same) -> BN -> ReLU -> MaxPool(2)
- Block 2: Conv1D(16, k=15, same) -> BN -> ReLU -> MaxPool(2)
- Block 3: Conv1D(32, k=15, same) -> BN -> ReLU -> MaxPool(2)
- Block 4: Conv1D(64, k=15, same) -> BN -> ReLU -> MaxPool(2)
- Head: Dropout(0.3) -> Flatten -> Dense(120, ReLU) -> Dropout(0.2) -> Dense(C, Softmax)
- Total Parameters: 49,687 (12 coeffs) / 65,047 (24 & 30 coeffs)
• frames144 Model (Temporal Sequence):
- Input: (N, 144, C) where C in {12, 24, 30}
- Pooling over time: 144 -> 72 -> 36 -> 18 -> 9 frames
- Flatten: 9 x 64 = 576 units into Dense(120)
- Total Parameters: ~104,000
Multi-Seed Experimental Summary
• Execution & Reproducibility Parameters:
- Optimizer: Adam, Learning Rate = 0.001
- Epochs: 100, Batch Size = 32
- Loss: Sparse Categorical Cross-Entropy
- Checkpoint: ModelCheckpoint monitoring val_accuracy (mode='max')
- Test Evaluation: Frozen checkpoint evaluated once on test split
• Verification & Testing:
- Automated unit test suite: tests/test_week4.py
- Confirms zero NaNs, correct tensor dimensions, valid split sizes, and strict speaker disjointness.
Notes: PRESENTER: All Team Members
SPEAKER NOTES:
Backup slide: Provides the exact parameter counts and layer configurations across both the baseline global pooling model and the 144-frame temporal model. Notice that frames144 almost doubles parameter count from 65k to 104k because of the larger flatten layer, which directly contributed to the rapid memorization and overfitting observed in Task 1.